## Slide 1: Optimising Breeder Blanket Design for Fusion Reactors
Semester 2 Masters Project Continuation
Vadan Khan
Rhodri Peters

## Slide 2: Project Introduction and Overview
Key research area for contemporary Fusion Projects
Our Approach: Neutron transport simulations
Semester 1 continuation
  Previously focused on material selection
Semester 2 focus: Optimising a Heterogeneous Design
  Fixed material choices to optimum from last semester
Novel Methodology: Algorithm to explore large parameter spaces faster
  Bayesian Optimisation

## Slide 3: Blanket Design
Heterogeneous (layered) blanket
4 Alternating breeder and coolant layers
Breeder: Eutectic Li17Pb93
Coolant: H20
Separators: Eurofer97 Steel
First Wall: Zircalloy

## Slide 4: Heterogeneous Effects
Compare heterogeneous breeder to homogeneous designs
Separator material added in homogenous and heterogeneous designs
Heterogeneous blankets have significantly lower TBR

## Slide 5: Linear Gradient Thickness Constraint
Linear gradient constraint imposed on layer thicknesses
Allows for study of front-loaded and rear-loaded designs
Reduces multi-variate problem to a single parameter.
Negative values front-loaded
Positive values rear-loaded

## Slide 6: TBR: Tritium Breeding Ratio
Total TBR ~constant
Breeding shifted to back layers if thickness backloaded

## Slide 7: Multiplication
Multiplication decreases for backloaded configurations

## Slide 8: Damage
Backloaded configurations suffer from greater separator damage
Frontloaded configurations suffer from greater front wall damage

## Slide 9: ML Theory: SOBO-GPR Iteration Loop
Simulated Test Data Pool
GPR Surrogate Model
SO Acquisition Function
Selected New Simulation
Approximated Optimum (at this iteration)
Best region to explore
Optimal Regions & Uncertainty
Add new test result to pool.
Improves future surrogate model approximations
SO: Single-Objective
BO: Bayesian Optimisation
GPR: Gaussian Process Regression
An ML (Bayesian Optimisation) method to run the minimal number of simulations for a maximum understanding of a parameter space

## Slide 10: ML Testing Examples
Final Iteration Surrogate Model + Uncertainty
Plots of the “true” function to find the maximum of
+
Points the Algorithm chose to sample

## Slide 11: Acquisition Function Tuning
“Greedy” tuning:
Search for peaks in regions that we have historically performed well
Explorative tuning:
Explore the wider parameter space to hunt for “hidden” peaks

## Slide 12: Optimal Configurations from BO studies
The optimiser consistently attempted to maximise breeder thickness (front first) and minimise coolant thickness (front first).

## Slide 13: ML Parameter Sensitivity
2D parameter sensitivity plots
  Offers deeper physical understanding
Compared B1 TBR contribution to other layers
Front layers are more impactful than rear layers
Demonstrates a clear “corner solution”.

## Slide 14: Conclusions  Next Steps
Optimal Design for TBR maximisation Clear:
  Maximise breeder and minimise coolants
Broaden study to investigate other materials
  Optimal results could be vary
Necessitates Holistic Study to balance other Parameters
  Heat extraction
  Material Damage
  Thickness / cost
SOBO-GPR Algorithm could support this research
  Modular to different materials & simulation functions
  Multi-Objective Optimisation could be implemented to balance other parameters

## Slide 15: BACKUP SLIDES

## Slide 16: Scattering vs Absorption Zeta Sweeps
Backloaded: Higher scattering but lower Absorption

## Slide 17: Scattering & Absorption Heat Maps
Also have bright peaks in separators

## Slide 18: Total Neutron Flux

## Slide 19: Heating per Source Neutron

## Slide 20: Damage Energy Zeta Sweep

## Slide 21: Layer-wise Heterogeneous TBR vs. Thickness