## Slide 1: TBR Project Report
Vadan Khan and Rhodri Peters
Notes: Good morning. I am Vadan, and this is my partner Rhodri. Today we are presenting our project on optimising the neutronic performance of fusion reactor breeder blankets. We utilised a coupled computational workflow to investigate how material choices and reactor geometry influence the production of Tritium fuel.

## Slide 2: Introduction to Fusion and Breeder Blankets
The Problem: No natural Tritium supply for D-T Fusion.
The Solution: Breed fuel in-situ:
Target: Tritium Breeding Ratio (TBR) > 1.1.
Challenge: 1-to-1 neutron economy requires (n, 2n) multipliers.
Notes: The Deuterium-Tritium fuel cycle is the most viable path for fusion, but while Deuterium is abundant, Tritium does not exist naturally. We have to breed it inside the reactor. The breeder blanket intercepts fusion neutrons to transmute Lithium into Tritium. However, because one fusion reaction produces only one neutron, and we lose neutrons to leakage and structure, we need a TBR greater than 1—ideally 1.1 to account for inefficiencies. This requires using neutron multipliers like Lead or Beryllium to ensure we get enough neutrons to sustain the fuel cycle.

## Slide 3: OpenMC and Simulation
Monte Carlo Transport (OpenMC):
Simulates stochastic particle histories.
Probabilistic interaction physics (ENDF/B-VIII.0).
Physics:
14.1 MeV Source (Muir Distribution).
Reflective Boundary Conditions (90° sector).
Accuracy: Particles N ~ 10^7 for <1% relative error.
Notes: To solve the Boltzmann Transport Equation for complex 3D geometries, we used the Monte Carlo code OpenMC. Instead of solving average fluxes, this method simulates millions of individual particle histories—rolling the dice on interaction probabilities for scatter, capture, or multiplication. We modelled a 90-degree sector of a tokamak with a 14.1 MeV neutron source. By running $10^7$ particles, we achieved statistical relative errors below 1%, ensuring our results are robust.

## Slide 4: Methodology
Coupled Workflow: Paramak (CAD) → DAGMC → OpenMC.
Parametric Sweeps:
Automated geometry reconstruction.
Variables: Material composition, Enrichment, Thickness, Coolant %.
Base Model:
Source: 14.1 MeV Ring.
First Wall: Zr-4 (Low absorption).
Notes: A major gap in current literature is the disconnect between geometry and material studies. Our methodology bridges this using a coupled workflow. We used Paramak to procedurally generate 3D CAD models, which were passed directly to OpenMC via the DAGMC format. This allowed us to run automated parametric sweeps—varying blanket thickness, enrichment, and coolant fractions systematically—rather than just analysing a single static design point.

## Slide 5: Liquid and Solid Breeder Results
Liquid Lead-Lithium ($Li_{17}Pb_{83}$):
TBR: 1.61 (Highest).
Mechanism: High density + Pb(n,2n) multiplication.
Solid Ceramics ($Li_4SiO_4$, etc.):
TBR: ~1.48 (Consistent).
Mechanism: Rely on Beryllium multiplier.
Molten Salts (FLiBe):
TBR: ~1.15 (Lower, but no MHD issues).
Notes: We first compared the major breeder classes. The liquid eutectic $Li_{17}Pb_{83}$ was the clear winner, achieving a TBR of 1.61. This is driven by the high packing density of the eutectic and the excellent neutron multiplication of lead. Solid ceramics were remarkably consistent at around 1.48, limited largely by the void space in pebble beds. Molten salts like FLiBe performed worse, barely clearing the self-sufficiency threshold, but they offer engineering advantages like reduced magnetohydrodynamic drag.

## Slide 6: Material Composition Results
Isotopic Enrichment (^6Li):
Saturation point at ~40%.
100% enrichment lowers TBR.
Reason: Loss of ^7Li(n, n'\alpha)T contribution.
Coolant Effects:
Water: Moderates neutrons → increases capture cross-section.
Gas (He, N_2): Acts as void → increases leakage.
Notes: One of our most significant findings concerns isotopic enrichment. While it is often assumed that 'more is better,' we found a saturation point at roughly 40% $^6Li$. Beyond this, the TBR plateaus and eventually drops. This is because at 100% enrichment, you completely remove $^7Li$, which provides a small but vital source of secondary neutrons via its own breeding reaction. We also found that Water is neutronically superior to Helium as a coolant because it acts as a moderator, slowing neutrons down to thermal energies where the breeding cross-section is highest.

## Slide 7: Blanket Structure Results
Radial Build Optimisation:
TBR saturates at 500–600 mm.
Physics: Neutron Mean Free Path $\lambda \approx 5.5$ cm.
Thickness > 60cm is "dead weight".
First Wall Impact:
TBR degrades linearly with wall thickness.
Trade-off: Zr-4 is neutronically ideal; Steel (EUROFER) is structurally required but penalty is ~0.15 TBR.
Notes: Geometrically, we determined the optimal blanket thickness. The TBR rises rapidly and saturates between 500 and 600 mm. We calculated the neutron mean free path in the blanket to be roughly 5.5 cm, meaning a 500 mm depth represents about 9 mean free paths—enough to attenuate over 99.9% of the flux. Increasing thickness beyond this adds weight and cost without adding fuel. We also quantified the penalty of the First Wall; while Zirconium is transparent to neutrons, realistic steel walls impose a TBR penalty of about 0.15.

## Slide 8: Conclusions
Optimal Design: Li_{17}Pb_{83} with Water coolant.
Key Findings:
Max TBR: 1.61.
Enrichment Saturation: 40% (Save costs).
Geometric Limit: 600 mm.
Critical Evaluation:
Neutronic optimum (Water + LiPb) = Chemical Safety Risk.
Neutronic optimum (Zr-4) = Structural Risk.
Future Work: Heterogeneous geometry (streaming effects).
Notes: In conclusion, our simulations identify $Li_{17}Pb_{83}$ as the superior breeding medium. We demonstrated that costly high-enrichment levels are unnecessary, as performance saturates at 40%. Physically, the blanket only needs to be 60cm thick to capture the full neutron flux. However, we must critically evaluate these results: our 'optimal' neutronic design uses water coolant and liquid lithium, which is a dangerous chemical combination. Real-world reactor design will likely have to sacrifice some of this neutronic performance for safety and structural integrity.